## Slide 1: Intro to Embedded Rust
Hackaday Supercon 2025
Get started: github.com/ShawnHymel/workshop-embedded-rust

## Slide 2: Agenda
About Rust
Exercise 1: Blinky
Exercise 2: Ownership and Borrowing
Exercise 3: I2C Temperature Sensor
Get started: github.com/ShawnHymel/workshop-embedded-rust

## Slide 3: Prerequisites
Working with microcontrollers
  Arduino
  MicroPython
  CircuitPython
Better: C/C++ with vendor tools
  STM32
  ESP-IDF
Memory management
  Stack vs. heap
  Pointers in C/C++

## Slide 4: Bad C
int* ptr = malloc(sizeof(int));
*ptr = 42;
...
free(ptr);
printf("%d\n", *ptr);
Undefined behavior
Do this to prevent
memory leaks

## Slide 5: Brief History of Rust
2006: Graydon Hoare begins designing Rust as a personal project
“Blackberry Leaf Rust Fungus” by John Tann,
used under CC BY 2.0 (Wikimedia Commons)
2010: Ownership system added
2009: Mozilla officially sponsors the Rust project
2012: v0.1 released. Original OCaml compiler rewritten in Rust
2013: Garbage collection removed. Hoare steps down. Core team of 6.
2015: v1.0 released. Core features and API stabilized.
2021: Rust Foundation formed with AWS, Google, Huawei, Microsoft, Mozilla
2020: Mozilla lays off 250 employees, disbands Servo team
2011: Logo

## Slide 6: Memory Management Tradeoffs
 | Examples | Pros | Cons
Manual memory management | C, C++ | Fast runtime (no overhead) Predictable performance Smaller program size | Error prone (runtime bugs) Development complexity (track allocations)
Garbage collection | Python, Java, JavaScript | Safe (no/fewer memory bugs) Automatic cleanup (faster development) | No low-level memory control Slower and unpredictable performance Larger program size
Ownership model | Rust | Safe (no/fewer memory bugs) Faster runtime (no/smaller overhead) Smaller program size | Development complexity Learning curve (understanding the borrow checker)

## Slide 7
let s1 = String::from("hello");
let s2 = s1;
// println!("{}", s1);
println!("{}", s2);
Ownership Model
Each value in Rust has an owner
There can only be one owner of a value at a time
When the owner goes out of scope, the value will be dropped
s1 “owns” the string
Ownership is moved from s1 to s2
This would cause a compile error!
This prints the contents of s2

## Slide 8
fn say_hello() {
let s1 = String::from("hello");
let s2 = s1;
println!("{}", s2);
}
Ownership Model
Each value in Rust has an owner
There can only be one owner of a value at a time
When the owner goes out of scope, the value will be dropped
s2 goes out of scope, so the string data is dropped (memory is freed)

## Slide 9
Systems Language
Manual memory management
Direct hardware control
Zero-cost abstractions
Predictable performance
Inline assembly support

## Slide 10
Rust Limitations
Steep learning curve
Slow development time
Slow compile times
  Borrow checker
  Generate copies of generics (monomorphization)
  Traits system
Large binary sizes
  Static linking by default
  Monomorphization
  Standard library

## Slide 11
Rust Limitations
No stable application binary interface (ABI)
  ABI: low-level specification that defines how compiled components communicate (specific to CPU architecture and OS)
  C has a widely-adopted, stable ABI
  Other languages can easily call programs/written in C
  Rust ABI not standardized, so other languages can’t call Rust libraries
  Workaround: expose a C-compatible interface
  Limits Rust’s growth and adoption

## Slide 12
Embedded Rust Limitations
Relatively new ecosystem
  Breaking changes in libraries
  Cargo helps manage dependencies
Limited official silicon vendor support
Lack of mature drivers and libraries
No mature RTOS option
  Embassy – async framework
  RTIC – interrupt-based concurrency framework
Smaller knowledge base and community than embedded C

## Slide 13: Exercise 1: Blinky
github.com/ShawnHymel/workshop-embedded-rust

## Slide 14: Exercise 2: Ownership and Borrowing
github.com/ShawnHymel/workshop-embedded-rust

## Slide 15: Pointers and References
fn main() {
let x = 42;
let raw_ptr: *const i32 = &x;
let reference = &x;
println!("x lives at: {:p}", &x);
println!("raw pointer: {:p}", raw_ptr);
println!("reference: {:p}", reference);
}

## Slide 16: Pointers and References
fn main() {
let x = 42;
let raw_ptr: *const i32 = &x;
let reference = &x;
println!("x lives at: {:p}", &x);
println!("raw pointer: {:p}", raw_ptr);
println!("reference: {:p}", reference);
}

## Slide 18: Pointers and References
struct SensorReading {
value: u16,
timestamp_ms: u32,
}
name | value
ptr | 
name | value
value | 4
timestamp_ms | 100
my_ref
reading

## Slide 19
Each value in Rust has an owner.
There can only be one owner at a time.
When the owner goes out of scope, the value will be dropped.
You can have either one mutable reference or any number of immutable references.
References must always be valid.
If you move out part of a value, you cannot use the whole value anymore.
Slices are references to the whole value and follow the same borrowing rules.
Ownership and Borrowing Rules